## Slide 1: LASER Light Amplification by Stimulated Emission of Radiation

## Slide 2: contents:-
Introduction
Stimulated absorption
Spontaneous emission
Stimulated emission
Population inversion
Einstein’s coefficient and Einstein’ relation
Characteristics of laser
Main parts of a laser
Different types of laser
Applications of laser

## Slide 3: Introduction:-
The word laser is an acronym that stands for “light amplification by the stimulated emission of radiation”
Stimulated emission was postulated by Einstein in 1917.
In 1960 , a solid state ruby laser is developed by maiman.
In 1961, a gas state He-Ne laser is developed by Ali javan and others in Bell telephone laboratory.

## Slide 4
Continued…….
From the theory of interaction of radiation with matter, we can get an idea regarding the working of laser.
we know that a laser beam is an intense, concentrated, monochromatic beam of light. The principle of laser is that, through artificial means(at a given time), the number of atoms in an excited state(usually referred to as the metastable state) of an element is made to be much higher than that in the ground state, resulting in the emission of a coherent, monochromatic laser as these atoms de-excite together.
The reason behind the longer lifetime of the atoms in the metastable state can be understood by Heisenberg’s uncertainity principle.
i.e. ΔE. ΔT > ћ
Consider an atom has two energy levels, E1 & E2. when it is exposed to radiation having a stream of photons, each with energy hν, three distinct processes can take place – Absorption, spontaneous emission & stimulated emission.

## Slide 5: Induced absorption(stimulated absorption)
The process in which an atom sized system in lower energy state is raised in to higher energy state by absorbing EM radiation which is quanta of energy is equal to the difference of energy of the two states is called stimulated absorption.
i.e.,
Before
After
E2
E1
E2
E1
hν = E2 - E1

## Slide 6
The probability of occurance of this absorption from state 1 to state 2 is proportional to the energy density u(ν) of the radiation.
P12=B12 u(ν)
where the proportionality constant B12 is known as the Einstein’s coefficient of absorption of radiation.

## Slide 7: Spontaneous emission:-
Atom in ground state
Atom in excited state
Before After emission
E2
E1
If an atom is initially in the upper state E2, it can come down to lower state E1 by emitting a photon of energy hν. This is known as spontaneous emission. This is the natural radiation decay process.
hν

## Slide 8
The probability of occurance of this spontaneous emission transition from state 2 to state 1 depends only on the properties of state 2 and 1 and is given by
P’21=A21
where A21 is known as the Einstein’s coefficient of spontaneous emission of radiation.
Einstein was the first to point out a third possibility of induced emission in which an incident photon of energy hν causes a transition from upper energy state E2 to lower energy state E1.

## Slide 9: Stimulated emission:-
According to Einstein, an atom in the excited energy state may, under the influence of the EM field of a photon of frequency ν incident upon, it jumps to lower energy state emitting an additional photon of same frequency (ν).Hence two photons , one original and the other emitted, move together.
Excited state
Ground state
E1
E2
Before After
i.e.
E2 – E1 = h ν

## Slide 10: Continued…….
The direction of propagation, phase, energy and state of polarization of the emitted photon is exactly same as that of incident stimulating photon so the result is an enhanced beam of coherent light.
The probability of occurance of stimulated emission transition from upper energy state E2 to lower energy state E1 is proportion to the energy density u(ν) of the radiation & is expressed as
P”21=B21 u(ν)
Where B21 is the Einstein’s coefficient of stimulated emission of radiation.

## Slide 11: Continued……
Thus, total probability of emission transition from the upper level 2 to lower level 1 is given by
P21 = P’21+ P”21
Or
P21 = A21 + B21 u(ν)

## Slide 12: Population inversion:-
In a system of atoms in thermal equilibrium hν =E2 - E1, the no. of atoms in the ground state is generally much greater than in a higher energy state. This is known as normal population inversion of atoms among the available energy states.
A state in which the no. of atoms in higher energy state is greater than that of lower energy state is known as population inversion.
The concept is of fundamental importance in laser science because the production of a population inversion is a necessary step in the workings of a laser.

## Slide 13: Einstein's coefficient and Einstein's relation:-
Let N1 & N2 be the no. of atoms at any instant in the state 1 and 2 respectively. The probability of absorption transition for no. of atoms from state 1 to 2 per unit time is given by
N1P12=N1B12 u(ν) ………………(1)
The total probability of transition for no. of atoms from state 2 to 1 ,either by spontaneously or by stimulated emission per unit time is given by
N2P21 = N2 [A21+B21 u(ν)]………….(2)

## Slide 14
In thermal equilibrium at temp. T , the absorption and emission probabilities are equal and thus we can write
N1P12 = N2P21
N1B12 u(ν) = N2[A21 + B21u(ν)]
u(ν)=N2A21/N1B12-N2B21
u(ν) =A21/B21[(N1/N2)(B12/B21) - 1]
But acc. to Einstein, B12 = B21
hence , u(ν)=A21/B21(N1/N2 - 1)

## Slide 15
Acc. To Boltzmann’s law the distribution of atoms among the energy states E1 and E2 at the thermal equilibrium at temp. T is given by
or
Here k is the Boltzmann constant. So,

## Slide 16
Planks radiation formula yields the energy density of radiation u(v) as
Comparing these equations we get
This shows the relation between the Einstein’s coefficients A21 & B21 which also shows the probabilities of spontaneous & stimulated emissions.
i.e. acco. to eqn (5), ratio of Einstein’s coefficients is proportional to cube of frequency which means probability of spontaneous emission increases rapidly with the energy diff. between the two states.
(5)

## Slide 17: Principle of laser:-
Let us consider an assembly of atoms of some kind that have metastable states of excitation energy hν.
The important requirement to achieve the laser action is that there should be more atoms in the meta stable state than in the ground state.
If this condition is achieved, there will be more stimulated emissions from atoms in the metastable state than induced absorptions by atoms in the ground state.
The step by step process that takes place in laser action are:-

## Slide 18
Step-1:- Atoms in the ground state are pumped to state E2 by photons of energy hν’=E2-E0 ,where ν’ is the frequency of incident radiation and E2,E0 are the energy of excited state and ground state respectively.(fig.a)
The step by step process that takes place in laser action are:-

## Slide 19
Step-2:- Rapid transition to metastable state E1 by spontaneous emission of photons of energy hν’’=E2-E1, where ν’’ is the frequency of emitted radiation and E1 is the energy of meta stable state(fig. b). This is non radiative transition.
These transitions follow hund’s rule.

## Slide 20
Step-3:- By this way more number of atoms are in metastable states.(fig.c) & fulfills the condition of population inversion.

## Slide 21
Step-4:- when photons of energy hν=E1-E0 are incident with the secondary photons themselves stimulating further transitions to produce an avalanche of coherent beam(fig.d) . This is known as induced emission.

## Slide 22
Continued…..

## Slide 23: Characteristics of laser:-
It is highly coherent.
It is monochromatic in nature.
Laser beam is collimated i.e hardly divergent.
Highly intense.
Highly directional.

## Slide 24
Main parts of a laser:-
Active medium or working substance
Pumping source or energy source
Resonant cavity/optical resonator

## Slide 25: Active medium or working substance:-
This is the basic material in which atomic and molecular transitions take place leading to laser action.
It is the medium where the stimulated emission take place.
Depending on the active medium lasers are classified into different types like solid, gas, dye or liquid, semiconductor laser.

## Slide 26: Pumping:-
The process of achieving population inversion is known as pumping of atom. Most commonly used methods are as follows:-
Optical pumping(used in ruby laser)
Electric discharge (used in He-Ne laser)
Inelastic atom atom collision.
Direct conversion ( used in semiconductor laser)
Chemical reaction(used in CO2 Laser)

## Slide 27
E3
E2
E1
hν21 = E2 - E1
Three level pumping:-
E1 level is the ground state, E2 and E3 are both excited state. The pumping process excites the atom to go to level E3 directly from E1
E3 - E1 = hνp
Where νp is the pumping frequency.

## Slide 28: Continued…
But E3 state is not a stable state and atoms undergo downward transition to E2 or E1.The transition E3 -> E1 is spontaneous. The probability of this transition is comparable to E3 -> E2.
E2 is a metastable state. At E2 , the spontaneous probability for E2 -> E1 transition is much less if the medium is exposed to frequency νp. The result is, the large accumulation of atoms at E2 level, hence population inversion is achieved.

## Slide 29
Now if an energy photon ν21 is used for triggering the transition E2-E1 following the equation hv21 = E2-E1 to produce stimulated emission of photon of energy hv21.

## Slide 30: Four level pumping:-

## Slide 31
The active centers are pumped from ground level E1 to the uppermost level E4 from where they readily fall to intermediate level E3 i.e metastable state, keeping level 2 empty.
Now level 3 is populated inversely w.r.t level 2. If a triggering incident beam has frequency v32 , the stimulated transition E3 to E2 is possible in chain.
The atoms from E2 to E1 may go spontaneously with non radiative transition.

## Slide 32: Resonant cavity:-
It is specially designed cylindrical tube
Set of mirrors at the ends of which are silvered one and being completely silvered at which the other is partially silvered
Photons are emitted parallel to the axis of the active medium which undergo multiple reflections between them
So, the light intensity can be increased.
Energy source
Working substance
Fully silvered
Partially
silvered

## Slide 33: Types of laser:-
Solid state laser ex.-Ruby laser
Gas laser ex.-He-Ne laser
Liquid laser
Semiconductor laser

## Slide 34: Ruby laser:-

## Slide 35: Construction:-
In ruby laser a cylindrical ruby rod made up of aluminum oxide which is doped with 0.05% weight of chromium oxide.
One end of rod is fully silvered and the other one partially silvered so it act as optical resonator.
The rod is surrounded by a glass tube which in turn is surrounded by the helical flash lamp filled with xenon gas.

## Slide 36: Working:-
When the flash lamp light will be flashed on ruby rod the chromium ions excited to higher energy states.
After staying for up to 10-8 second ions get transmitted to the metastable state.
The laser radiation of a wavelength of 6943A0 and laser emission is pulsed one.

## Slide 37: He-Ne Laser:-

## Slide 38: Construction:-
A He-Ne laser consists of large and narrow discharge tube filled with helium a and neon gases in the ratio 10:1.
The tube is enclosed between fully and partially reflective mirrors which serve as optical cavity.
The two end windows are set at Brewster's angle, so reflected radiations enter into the tube become polarized.

## Slide 39: Working:-
Helium atoms after transferring their energies to neon atoms are excited to 2s and 3s.
The population in theses levels is more than those in lower levels 2p and 3p.
The emission of radiation having wavelength 6328A0 is red in colour and it gives continuous emission of radiation.

## Slide 40: Semiconductor laser:-
In these lasers, junction diodes are used.
The doping of p-n junction diode is done.
Both the acceptors and donors are doped. These are known as ILD(Injection Laser Diodes).
Whenever the current is passed then the light modulation from the ILD can be seen. This is used in various electronic equipments

## Slide 41
DIAGRAM:-

## Slide 42: Applications:-
Modulated laser beam have been used for communication.
Lasers are used in medical field.
High power laser have been used for cutting & drilling holes in hard metal and diamonds.
They have been used in the production and research with holograms, they are also used in high speed photography and fiber optics.
Lasers are used in photodiode detection.
Laser are used in printers.
Lasers are used as barcode scanners in library and in supermarkets.

## Slide 43: Holography:-
Holography was invented by Denis Gabor in 1947.
Holography is a technique that allows the light scattered from an object to be recorded and later reconstructed so that it appears as if the object is in the same position relative to the recording medium as it was when recorded.
The image changes as the position and orientation of the viewing system changes in exactly the same way as if the object were still present thus making the recorded image appear 3 dimensional.

## Slide 44
In holography the light waves reflected from an object are recorded. This photographic record is called a hologram.
The hologram has no resemblance with the object, although it contains all information about the object in a kind of optical mode.
When it is illuminated by a coherent light source, a 3 dimensional image of the original object is formed.
The formation of image from hologram is known as the reconstruction process.

## Slide 45: working:-
Gabor recorded the wave pattern on a photographic plate by mixing 2 beams namely a reference beam and an object beam ( the beam reflected by the object) .
The object is illuminated by highly monochromatic and coherent light (laser beam) .

## Slide 46
Light is reflected from the to entire photographic plate. A part of the incident laser beam is made to fall on a plane mirror which reflects it toward the photographic plate. This is the reference beam.
The object beam reflected from the object interferes with the reference beam and produces an interference pattern on the photographic plate.
The photographic plate carrying the interference pattern is called a hologram.
This is also known as Gobar Zone Plate.