## Slide 1: Internet of Things VII Sem Dept of CSE, NIT Raipur Unit II IoT Protocols IoT Access Technologies Topic Application transport methods: SCADA
Dr. Veena Anand

## Slide 2: SCADA: Supervisory Control and Data Acquisition
Introduction:
SCADA is an acronym that stands for Supervisory Control and Data Acquisition.
SCADA refers to a system that collects data from various sensors at a factory, plant or in other remote locations and then sends this data to a central computer which then manages and controls the data.
SCADA systems are used not only in industrial processes: e.g. steel making, power generation (conventional and nuclear) and distribution, chemistry, but also in some experimental facilities such as nuclear fusion.

## Slide 3: SCADA: Supervisory Control and Data Acquisition
Introduction:
The size of such plants range from a few 1000 to several 10 thousands input/output (I/O) channels.
However, SCADA systems evolve rapidly and are now penetrating the market of plants with a number of I/O channels.
Definition of SCADA:
A collection of equipment that will provide an operator at remote location with enough information to determine the status of a particular piece of a equipment or entire substation and cause actions to take place regarding the equipment or network.

## Slide 4: SCADA: Supervisory Control and Data Acquisition
Introduction:
SCADA systems are used to monitor or to control chemical or transport processes in municipal water supply systems, to control electric power generation, transmission and distribution, gas and oil pipelines, and other distributed processes.
SCADA achieves this requirement collecting reliable field data through remote terminal units (RTUs) Intelligent Electric Devices (IEDs) and presenting them to user requirement.
The user interface or the man machine interface (MMI) provides various options of data presentation according to specific application and user needs.

## Slide 5: SCADA: Supervisory Control and Data Acquisition
Introduction:
There are many parts of a working SCADA system.
A SCADA system usually includes signal hardware (input and output), controllers, networks, user interface (HMI), communications equipment and software.
All together, the term SCADA refers to the entire central system.
The central system usually monitors data from various sensors that are either in close proximity or off site.
An industrial measurement and control system consisting of a central host or master (usually called a master station, master terminal unit or MTU).

## Slide 6: SCADA: Supervisory Control and Data Acquisition
SCADA Systems:
A SCADA system refer to a system consisting of a number of remote terminal units (or RTUs) collecting field data connected back to a master station via a communications system.
The master station displays the acquired data and also allows the operator to perform remote control tasks.
The accurate and timely data (normally real-time) allows for optimization of the operation of the plant and process.
A further benefit is more efficient, reliable and most importantly, safer operations.
This all results in a lower cost of operation compared to earlier non-automated systems.

## Slide 7: SCADA: Supervisory Control and Data Acquisition
SCADA Systems:
A successful SCADA installation depends on utilizing proven and reliable technology, with adequate and comprehensive training of all personnel in the operation of the system.
There is a history of unsuccessful SCADA systems – contributing factors to these systems includes inadequate integration of the various components of the system, unnecessary complexity in the system, unreliable hardware and unproven software.
Today hardware reliability is less of a problem, but the increasing software complexity is producing new challenges.

## Slide 8: SCADA: Supervisory Control and Data Acquisition
SCADA Systems:
It should be noted in passing that many operators judge a SCADA system not only by the smooth performance of the RTUs, communication links and the master station (all falling under the umbrella of SCADA system) but also the field devices (both transducers and control devices).
The RTU provides an interface to the field analog and digital signals situated at each remote site.
The communications system provides the pathway for communications between the master station and the remote sites.
This communication system can be radio, telephone line, microwave and possibly even satellite.

## Slide 9: SCADA: Supervisory Control and Data Acquisition
SCADA Systems:
The master station (and sub-masters) gather data from the various RTUs and generally provide an operator interface for display of information and control of the remote sites.
In large telemetry systems, sub-master sites gather information from remote sites and act as a relay back to the control master station.
SCADA technology has existed since the early sixties and there are now two other competing approaches possible – distributed control system (DCS) and programmable logic controller (PLC).
In addition there has been a growing trend to use smart instruments as a key component in all these systems.

## Slide 10: SCADA: Supervisory Control and Data Acquisition
SCADA Systems:
Distributed control system (DCS), is another variant of SCADA where data acquisition and control functions are performed by a number of distributed microprocessor-based units situated near to the devices being controlled or the instrument from which data is being gathered.
DCS systems have evolved into systems providing very sophisticated analog (e.g. loop) control capability.
A closely integrated set of operator interfaces (or man machine interfaces) is provided to allow for easy system configurations and operator control.
The data highway is normally capable of fairly high speeds.

## Slide 11: SCADA: Supervisory Control and Data Acquisition
Evolution of SCADA:
1890’s Remote Control and Remote Indication
1920’s Tele command and control
1930’s Check Before Operate (CEO)Systems
Based on Electro Mechanical Technology
1960’s Supervisory Control Systems (Remote Control & Status Indication)
1960’s Data Acquisitions gaming Popularity (DAS) SCADA came into being.
1980’s Load Dispatch Centre and Control
1990’s Energy Control Centre
2000’s Energy Management Systems

## Slide 12: SCADA: Supervisory Control and Data Acquisition
Objectives of SCADA:
The important objectives of SCADA are to listed below:
1. Monitoring : Continuous monitoring of the parameters of voltage , current, etc..
2. Measurement: Measurement of variables for processing.
3. Data Acquisition: Frequent acquisition of data from RTUs and Data Loggers / Phasor data Concentrators (PDC).
4. Data Communication: Transmission and receiving of large amounts of data from field to control centre’s.
5. Control: Online real time control for closed loop and open loop processes.
6. Automation: Automatic tasks of switching of transmission lines, etc.

## Slide 13: SCADA: Supervisory Control and Data Acquisition
Benefits of SCADA:
The important benefits of an EMS can be addresses as the following functions:
1. Continuous monitoring of process.
2. Real time control.
3. Automation and Protection.
4. Remote control and operation.

## Slide 14: SCADA: Supervisory Control and Data Acquisition
Functions of SCADA:
The important functions of an SCADA are listed below
1. Data Acquisition
2. Information Display
3. Supervisory Control
4. Alarm Processing
5. Information Storage and Reports
6. Sequence of Event Acquisition
7. Data Calculation
8. Special RTU Processing/Control

## Slide 15: SCADA: Supervisory Control and Data Acquisition
SCADA IN PROCESS CONTROL:
There are two types of process-control systems in view
i) distributed control systems (DCS) and ii) supervisory control and data acquisition (SCADA).
DCS are typically used for single-point processing and are employed in a limited geographic area.
On the other hand, SCADA systems are used for large-scale, distributed management of critical infrastructure systems and are often geographically dispersed.
For example, in a power utility, DCS may be used for generation of power, while SCADA is used for the distribution and transmission of power.

## Slide 16: SCADA: Supervisory Control and Data Acquisition
SCADA Applications:
SCADA is not a specific technology, but a type of application. SCADA stands for Supervisory Control
and Data Acquisition— any application that gets data about a system in order to control that system is
a SCADA application.
A SCADA application has two elements:
The process or system that needs to be monitored and controlled.
A network of intelligent devices that interfaces with the first system through sensors and control outputs.

## Slide 17: SCADA: Supervisory Control and Data Acquisition
SCADA systems are widely used for control in the following domains:
1. Electric power generation, transmission and distribution: Electric utilities use SCADA systems to detect current flow and line voltage, to monitor the operation of circuit breakers, and to take sections of the power grid online or offline.
2. Water and sewage: State and municipal water utilities use SCADA to monitor and regulate water flow, reservoir levels, pipe pressure and other factors.
3. Buildings, facilities and environments: Facility managers use SCADA to control HVAC, refrigeration units, lighting and entry systems.

## Slide 18: SCADA: Supervisory Control and Data Acquisition
SCADA systems are widely used for control in the following domains:
4. Manufacturing: SCADA systems manage parts inventories for just-in-time manufacturing, regulate industrial automation and robots, and monitor process and quality control.
5. Mass transit: Transit authorities use SCADA to regulate electricity to subways, trams and trolley buses; to automate traffic signals for rail systems; to track and locate trains and buses; and to control railroad crossing gates.
6. Traffic signals: SCADA regulates traffic lights, controls traffic flow and detects out-of-order signals.

## Slide 19: SCADA: Supervisory Control and Data Acquisition
Real-Time Monitoring and Control using SCADA
The following are the important features of a SCADA from an control point of view. SCADA is capable of the following:
1. Acquire quantitative measurements immediately and over time
2. Detect, Diagnose and correct problems as soon as they arise
3. Measure trends over time and prepare reports and charts
4. Discover and eliminate bottlenecks over time and improve efficiency
5. Ability to Control large and complex processes with a few specialized staff.

## Slide 20: SCADA: Supervisory Control and Data Acquisition
SCADA Functions:
A SCADA system performs four functions:
1. Data acquisition
2. Networked data communication
3. Data presentation
4. Control

## Slide 21: SCADA: Supervisory Control and Data Acquisition
These functions are performed by four kinds of SCADA components:
1. Sensors (either digital or analog) and control relays that directly interface with the managed system.
2. Remote telemetry units (RTUs). These are small computerized units deployed in the field at specific sites and locations. RTUs serve as local collection points for gathering reports from sensors and delivering commands to control relays.
3. SCADA master units. These are larger computer consoles that serve as the central processor for the SCADA system. Master units provide a human interface to the system and automatically regulate the managed system in response to sensor inputs.
4. Communications network that connects the SCADA master unit to the RTUs in the field.

## Slide 22: SCADA: Applications
1. Electric power generation, transmission and distribution: Electric utilities use SCADA systems to detect current flow and line voltage, to monitor the operation of circuit breakers, and to take sections of the power grid online or offline.
2. Water, Waste Water Utilities and Sewage: State and municipal water utilities use SCADA to monitor and regulate water flow, reservoir levels, pipe pressure and other factors.
3. Buildings, facilities and environments: Facility managers use SCADA to control HVAC, refrigeration units, lighting and entry systems.
4. Oil and Gas Trans & Distributions
5. Wind Power Generation

## Slide 23: SCADA: Applications
6. Communication Networks
7. Industrial Plans and Process Control
8. Manufacturing: SCADA systems manage parts inventories for just-in-time manufacturing, regulate industrial automation and robots, and monitor process and quality control.
9. Mass transit and Railway Traction: Transit authorities use SCADA to regulate electricity to subways, trams and trolley buses; to automate traffic signals for rail systems; to track and locate trains and buses; and to control railroad crossing gates.
10. Traffic signals: SCADA regulates traffic lights, controls traffic flow and detects out-of-order signals.

## Slide 24: SCADA: SCADA in Power Systems
SCADA is widely used in power systems. The applications for SCADA keep increasing day after day. Some of the applications are:
Comprehensive operational planning and control
Fuel resource scheduling
Optimum power flow
Network security
Economic dispatch
Generation dispatch control

## Slide 25: SCADA: SCADA in Power Systems
Expected Benefits of SCADA for Power Systems:
Improved quality of service
Improved reliability
Reduced operating costs
Maintenance /Expansion of customer base
Ability to defer capacity addition projects
High value service providers
Improved information for engineering decision

## Slide 26: SCADA: SCADA in Power Systems
Expected Benefits of SCADA for Power Systems:
value added services
Flexible billing option
Improved customer information access
Reduced system implementation costs
Reduced manpower requirements

## Slide 27: SCADA: Adapting SCADA for IP
In the 1990s, the rapid adoption of Ethernet networks in the industrial world drove the evolution of SCADA application layer protocols.
Benefits of this move to Ethernet and IP include the ability to leverage existing equipment and standards while integrating seamlessly the SCADA sub networks to the corporate WAN infrastructures.
To further facilitate the support of legacy industrial protocols over IP networks, protocol specifications were updated and published, documenting the use of IP for each protocol.

## Slide 28: SCADA: Adapting SCADA for IP
Like many of the other SCADA protocols, DNP3 (Distributed Network Protocol 3) is based on a master/slave relationship. The term master in this case refers to what is typically a powerful computer located in the control center of a utility, and a slave is a remote device with computing resources found in a location such as a substation.
DNP3 refers to slaves specifically as outstations.
Outstations monitor and collect data from devices that indicate their state, such as whether a circuit breaker is on or off, and take measurements, including voltage, current, temperature, and so on.

## Slide 29: SCADA: Adapting SCADA for IP
The IEEE 1815-2012 specification describes how the DNP3 protocol implementation must be adapted to run either over TCP (recommended) or UDP.
This specification defines connection management between the DNP3 protocol and the IP layers, as shown in next figure.
Connection management links the DNP3 layers with the IP layers in addition to the configuration parameters and methods necessary for implementing the network connection.
The IP layers appear transparent to the DNP3 layers as each piece of the protocol stack in one station logically communicates with the respective part in the other.

## Slide 30: SCADA: Adapting SCADA for IP

## Slide 31: SCADA: Adapting SCADA for IP
IN the previous figure, the master side initiates connections by performing a TCP active open.
The outstation listens for a connection request by performing a TCP passive open.
Dual endpoint is defined as a process that can both listen for connection requests and perform an active open on the channel if required.
Master stations may parse multiple DNP3 data link layer frames from a single UDP datagram, while DNP3 data link layer frames cannot span multiple UDP data grams.

## Slide 32: SCADA: Adapting SCADA for IP
Single or multiple connections to the master may get established while a TCP keepalive timer monitors the status of the connection.
Keepalive messages are implemented as DNP3 data link layer status requests.
If a response is not received to a keepalive message, the connection is deemed broken, and the appropriate action is taken.